## Slide 1
AIShopVision
Known product
in video
AIShop Sprint 001
Solution, code, and test walkthrough
Revision 06 / working tree / 20 September 2026
Notes: Welcome. This walkthrough explains the first foundation for AIShopVision: a small, testable way to notice one known product while a prerecorded video is still playing.
We begin with the intent, then the user journey and test strategy. The concrete reference is the banana image shown on the next slide. The positive fixture contains that banana; the negative fixture does not. The system must raise a provisional signal only when its evidence supports it.
Only after that context do the four chapters move into architecture, frame analysis, episodes and evidence, and verification. The HITL, Human in the Loop, reviews the evidence and observes the final physical-iPhone run. Live camera capture and general object detection remain outside this sprint.

## Slide 2
Sprint intent
A provisional signal while frames are still arriving
User need
Notice when a known product may be visible.
Increment
Analyze frames before the video finishes.
Result
Show possible match and retain the strongest evidence.
Boundary
One local target. Prerecorded video. Entirely local.
Code:
Pipeline
02
Notes: This sprint gives a user an early, provisional signal that one known product may be visible while a prerecorded video is still playing. The goal is timely evidence, not general object recognition.
The next slide introduces the concrete experiment: two recorded fixture videos with different expected outcomes. That visual example makes the words target, possible match, and control precise before we discuss the user journey.
The pipeline keeps the strongest evidence and summarizes the session without reading the video again. A feature-print distance remains provisional. This sprint provides neither object boxes nor a live camera.

## Slide 3
The two videos under test
A target case and a no-target control before the diagnostic journey
The fixture choice gives the test a clear expected outcome.
Positive fixture
Banana appears
Expected: possible-match episode
Control fixture
No banana appears
Expected: no false candidate
Both are local recorded videos. The diagnostic journey begins only after this choice.
Code:
Fixture annotations
Fixture resources
Harness screen
03
Notes: The last slide stated the intent. This slide makes the experiment concrete before the walkthrough uses the word banana again. The system receives one prerecorded video at a time.
The positive fixture is a kitchen video. In its annotated expected interval, the banana appears in frame. That is the target case. The negative fixture is a different kitchen video with no banana. It is the control case.
Both fixtures enter the same local production pipeline. The expected difference is a possible-match episode for the positive video and no false candidate for the negative video. The next slide shows how the HITL selects one of these videos, observes the run, and keeps the evidence.

## Slide 4
How to test
Three layers of evidence with different boundaries
Mac pipeline gate
./e2e/ios/run.zsh
Real video, real Vision, production pipeline, both fixtures
Simulator app tests
AIShop-VisionDiagnostics scheme
Startup isolation and harness-model behavior
Physical iPhone
Both fixtures and exported logs
Required demonstration and host comparison remain pending
Package integration is not full app-and-device end-to-end acceptance.
Code:
Mac gate
Integration tests
App tests
04
Notes: Start with the Mac integration gate. It runs the package tests with real Vision and verifies that every required test actually executed. This covers the production analysis pipeline with recorded video as its input edge.
The Simulator tests answer a different question: whether diagnostic startup bypasses normal services and whether the harness model handles its states. The saved app-test snapshot has twenty-five passing tests. It does not establish working Vision inference on the Simulator.
The final layer is a physical iPhone run observed by the HITL, Human in the Loop, followed by comparison of exported logs. These layers complement each other. Neither a package pass nor an app build can stand in for device acceptance.

## Slide 5
High-level architecture
Shared processing with separate hosts and evaluation
Mac tests or iPhone debug harness
Select local inputs and call the same pipeline
Frame stream and target catalog
Timestamped images and one cached reference feature
Scorer
Whole-frame and central-crop Vision distances
Episode aggregator
Require repeated support and retain the strongest frame
Recorder and report
Ordered events, replayable report, separate JPEG evidence
The annotation evaluator stays outside the production package.
Code:
Core package
Harness
Evaluator
05
Notes: Read this architecture from top to bottom. Mac tests and the iPhone debug harness are hosts around the same production pipeline.
The frame stream supplies timestamped images. The local catalog supplies the reference feature. The scorer measures visual distance, and the aggregator decides when repeated support forms an episode.
The recorder feeds an ordered log and a report builder. Images live separately, so the log stays structured and can rebuild report data without carrying image bytes.
The evaluator belongs to a separate development target. It knows the annotation zones used to judge the fixtures. The production package never sees those answers. This separation helps us test behavior without teaching the application the expected result.

## Slide 6
One frame through the pipeline
The order of work is also the order of evidence
Receive and sample
Record whether the decoded frame is eligible
Measure
Produce whole-frame and crop distances
Aggregate
Open, update, or close a candidate episode
Retain and record
Save best-image evidence before logging its episode event
Publish
Send the latest score, signal, and metrics to the host
First update arrives before EOF. The pipeline never needs a second video pass.
Code:
Pipeline source
Recorder
Pipeline tests
06
Notes: A sampled frame follows one path through the pipeline. The stream first records decoded frames and sampling decisions. For an eligible frame, the pipeline logs the sample and asks the scorer for measurements.
It logs the score before the aggregator consumes it. If an episode opens or its best frame changes, the pipeline saves the selected image and records the episode event. Only then does it publish an update to the host.
This order makes the live result explainable from the event log. A test checks that the first update occurs when only the first decoded frame has arrived. Another replays the saved log and compares it with the live report. These are direct checks of incremental behavior and evidence consistency.

## Slide 7
Concurrency and ownership
Analysis work stays outside the UI actor
UI on the main actor
Start one run and display published updates
Detached pipeline worker
Coordinate scoring, episodes, images, and reporting
Optional paced producer
One consumer plus one replaceable pending frame
Serialized recorder
Concurrent callbacks share one append-and-update lock
Main-actor update
Generation token rejects results from an obsolete run
Caller cancellation reaches both the stream and detached worker.
Code:
Pipeline
Recorder
Harness model
07
Notes: Concurrency matters because frame production and image analysis must not freeze the interface. The flow starts on the main actor, hands analysis to a detached pipeline worker, and returns updates to the main actor.
Deterministic mode waits for each frame to finish. Paced mode adds a producer and a one-frame pending buffer. Stream callbacks can therefore overlap analysis. The recorder serializes logging and report updates so both see the same event order.
The harness uses a generation token to prevent an old run from replacing a newer run's state. Caller cancellation reaches both the stream and worker. The linked tests verify that pipeline updates originate outside the main thread, while the harness owns UI state.